| Stillwater Billings Clinic | POLICY MANUAL Portable Ultrasound Guideline Effective Date: 10/26/2016 Policy #: Approved by: |
| --- | --- |

TITLE:  Portable Ultrasound Guidelines

POLICY STATEMENT:

This guideline is to support the proper use and care of the Mindray DP 50 Ultrasound Machine.

INTENT:  It is the intent of this policy to be document to insure the proper use and care of the Mindray DP 50 Ultrasound Machine.

PRACTICE:  This policy is to be used for medical practice in the Emergency Department and in Acute Care at Stillwater Billings Clinic.

PROCEDURE:

- Equipment Care

  - Maintenance:

    - The Radiology department will be responsible for ensuring that the Mindray DP 50 ultrasound unit is functioning properly.

      - This includes the initiation and monitoring any maintenance contract needed for the device after the expiration of the warranty.

    - Equipment performance monitoring will be completed on the unit by Intermountain Biomedical during their quality control visits to this facility, first check was completed on 06/23/2016.

    - Image quality for the device will be monitored by Northwest Ultrasound during the yearly maintenance visits.

    - All care will be taken to prevent damage to the device and ensure that the ultrasound probes are not struck or dropped on the floor.

  - Cleaning:

    - Cleaning of this device will be done with Protex Ultra (One-Step Cleaner/Disinfectant/Sanitizer).  This will be kept with the unit and a backup supply of the product will be located in Central Supply.  Cidex or Purple Disinfectant wipes are NOT to be used to clean this device.

      - Wipe the surface area thoroughly until wet and all it to remain wet for 4 minutes.

      - Allow the cleaning product to air dry.

    - Probe covers are to be kept with the unit and used in the event of exposure to body fluids.

  - Storage:

    - The Mindray DP 50 Ultrasound unit will be stored in the Emergency Department and remain covered when not in use.

- Exam Procedures:

  - FAST Exams: To evaluate the torso for evidence of traumatic free fluid exam is to be done by the medical provider only to aid in the decision making process regarding further evaluation or testing, clinical management, and therapeutic management.

    - Training:  This exam can be completed by physicians and mid-level providers that have completed FAST Exam Ultrasound Training for Medical Professionals.

    - Documentation:

      - An image from the exam should be printed, labeled with two patient identifiers (a patient identification label is sufficient), and scanned into the EMR.

      - Clinician charting will be accessible in CERNER and is to include the provider’s notes of patient care.

  - Bladder Scanning: To determine bladder volume by a non-invasive method assisting providers in determining the need for urinary catheterization.

    - Training:

      - Staff who have been trained to use the Mindray DP 50 for bladder scanning may use the ultrasound.

      - This exam can be performed by CNAs, LPNs, RNs, NPs, PAs, and Physicians.

    - Documentation:

      - An image from the exam should be printed, labeled with two patient identifiers (a patient identification label is sufficient), and scanned into the EMR.

      - The Clinician performing the exam will chart the bladder scan volume within the Genitourinary Flow Sheet in CERNER.

  - Ultrasound Guided Venous Access:  To provide enhanced capability to procure peripheral intravenous access for patients within this facility.

    - Training:

      - All RNs, LPNs, PAs, NPs, and Physicians who are trained can use the ultrasound to gain venous access.

    - Documentation:

      - A Duo image from the exam should be printed, labeled with two patient identifiers (a patient identification label is sufficient), and scanned into the EMR.

      - This image is to include the image of the vessel (vein) to be accessed and the vessel “wink” to show that it is not an artery prior to access.

      - Clinician charting of the intravenous access in CERNER should indicate that ultrasound guidance was used.  Details of the insertion is to include catheter size, site and location, and attempts needed for access.